## Slide 1
CS447 Recitation #8: 7/11/18
Agenda for today:
Overview of Lab #8
Be sure to sign in!
  These slides are available online:
  https://github.com/kc13/CS447

## Slide 2
Lab #8 overview: Building an ALU
Assignment Breakdown:
Part 1: Build a one-bit ALU
Page 2: Build a multibit ALU
Page 3: Interface with the multibit ALU from an outer “main” circuit

## Slide 3
Lab #8, Part 1: Build a one-bit ALU
Can perform:
AND,
OR,
NOR,
addition,
subtraction, set if less than (slt)
seven inputs
a, ~a, b, ~b, carryIn, operation
Less:
- for setting the
LSB for slt output
- when 1-bit ALUs are chained to produce a multibit ALU,
the other “Less” inputs will be
hard-wired to 0
three outputs
Result
Carryout
Not shown: Set
  For setting the LSB for slt output
  When 1-bit ALUs are chained together to produce a multibit ALU, the “set” output is only meaningful for the MSB (and will be used to set “Less” for the LSB)

## Slide 4
Lab #8, Part 2: Build a multi-bit ALU
Chain together 8 of the 1-bit ALUs (which will be prepared as a different subcircuit)
Note “set” output from MSB is fed into Less input for LSB; other Less inputs are set to constant values of 0.

## Slide 5
Lab #8, Part 2: Build a multi-bit ALU
Multibit subcircuit inputs:
  Four bit ALUOperation code, to be broken down (i.e., via splitter) into:
    Ainvert (for setting Ainvert in the individual bits)
    Bnegate (for setting Binvert and CarryIn for the individual bits)
    Operation (goes to the operation MUX in each bit)
Multibit subcircuit outputs:
  8-bit result
  1-bit “zero” output (indicates if the result is 0)
  1-bit overflow output
    Will require some logic to figure out if there is overflow or not (see slides 59-60 of ALU slide deck)
    “set” output from MSB may need to be adjusted if overflow is present (see slide 61)

## Slide 6
Lab #8, Part 3: Interact with the multibit subcircuit from the main canvas

## Slide 7
Submission
For demos in recitation:
    Show the completed circuits.
    Demonstrate accurate output for a variety of different operations (especially those which are relatively complex, such as set less than)
Remember to sign in!