## Slide 1
CS447 Recitation #9: 7/18/18
Agenda for today:
Overview of Lab #9
Please sign in!
  These slides are available online:
  https://github.com/kc13/CS447

## Slide 2
Lab #9 overview: Building a Register File
Specifications:
Similar to registers in MIPS / MARS, except only 8:
  32-bit wide data
  Can write one register at a time
  Can read from two registers at a time

## Slide 3
Lab #9 overview: Inputs to / outputs of the Register File
8 of them (see next slide for Register component info)
Indices to choose which two registers to read (0-7).
Index to choose destination register
Data to write to destination register
Data read from the rs and rt registers
Required input to all registers, see “Wiring”
Allows for the write to actually take place (otherwise, destination register and data are ignored)
Crossed lines imply bit width > 1

## Slide 4
Lab #9: Registers in Logisim
Output
Input
Enable:
1-bit input, 1 = allow write, 0 = disable write
“Clear”, not needed here
Bit width may be set in attribute panel
(default is 8 bits; note values are displayed in hexadecimal)
Clock input
Trigger attribute: should be set to “Falling Edge” for all registers.

## Slide 5
Lab #9: Decoders and ANDs for write register (rd) selection
This illustrates how writes are done for the first 4 of 32 registers.
The “enable” and “write data” pins of all registers will receive inputs on every clock tick.
Each AND gate will determine (1) whether writes are permitted on this cycle, and (2) whether the specific register is the destination of the write.
The decoder translates the register number so that a 1 bit is routed to the chosen register, and a 0 bit elsewhere.

## Slide 6
Lab #10: Decoder in Logisim (see “Plexers”)
In Attribute Panel, adjust “Select Bits” to 3 (to allow for 000 to 111).
The grey dot marks the pin where you will input this 3-bit value.
The other pin on the bottom should be irrelevant here.
The eight outputs should be routed to the 8 different registers. Only one of them should carry a ‘1’ value at any given time.

## Slide 7
Lab #9: Multiplexers for selecting registers to read
Note that the figure depicts 32 registers instead of 8.
Each register should send its output to both MUXes.
Make sure to adjust the data bit width of the multiplexers, and also the Select Bits attribute.

## Slide 8
Lab #9: Testing
The Poke tools can be used on input pins, the register, and the clock.
Simulate/Ticks Enabled will set the clock to run on its own.

## Slide 9
Completion during recitation:
  You will be asked to demonstrate that both reads and writes occur appropriately.
  Assignments must be submitted via Courseweb, even if checked off during recitation.
  Please remember to sign in!